# This guide is a quick introduction to AP's Toolkit.
The guide is for Version 1.0 of library.
There is following modules, that mostly interconnect with each other:
- ap_net - networking functions. Contains TCP/UDP connections pool and epoll()-based helpers
- ap_log - logging and debugging facilities. Contains log messages broadcasting tools. Error control for toolkit
- ap_str - strings manipulation. Mainly strtok() wrapper
- ap_utils - Miscellaneous utility functions that not falls into above categories.
# Section 1. ap_net module. Connections pool
This module have one big system: connections pool. That is for client-server communication via TCP or UDP messaging. You can use almost all functions directly, controlling pool's connection list with manual accept/receive/send/close. But intended use is partly or fully asynchronous, so you setup pool and cycle poll function, that will take the burden of calling secondary service procedures as accept/receive or close and notifying your callback function of pending events. The callback function will receive signals for all aspects of socket activity that may require special attention. This include new connection or data arrival, connection errors and expiration, etc.
So the usage pattern on server side, where we have listener socket is to create pool, create listener, while(something) do_poll().
Client side is the same, but instead of listener we do connect() between polls.
For simplicity reasons each server-type pool can have just one TCP or UDP listener port, and also server pool's incoming connections are limited to either IP v4 or v6 - which is set in pool's flags. The client's pool with only outgoing connections ignore those restrictions. Of course you can have as much pools of any kind as you wish. The trick is you can have single callback function for all of them, so there is really no big difference in management one or many pools.
Now to real part. We begin with creating pool:
struct ap_net_conn_pool_t *pool;
pool = ap_net_conn_pool_create(POOL_FLAGS, MAX_CONNECTIONS_SLOTS, DEFAULT_TIMEOUT_IN_MS, CONNECTION_RECEIVING_BUFFER_SIZE, callback_function);
- Where POOL_FLAGS bit set controls TCP or UDP, IPv4 or IPv6 modes, etc (see AP_NET_POOL_FLAGS_*)
- MAX_CONNECTIONS_SLOTS – is hard limit of possible simultaneous connections.
  You can lift or drop this number later via call to ap_net_conn_pool_set_max_connections()
- DEFAULT_TIMEOUT_IN_MS – for incoming connections there will be default expiration time set from this parameter value in milliseconds. Expired connections will be closed automatically in polling function. Callback will be notified before closing
- CONNECTION_RECEIVING_BUFFER_SIZE – each connection in pool have individual buffer for incoming data. This is how many bytes will be there.
  Set it thoughtfully. The dirty part is you are required to behave with this buffer and obey some simple rules to get flawless data stream.
- And callback_function is our callback that gets just two parameters: connection's structure pointer and signal type.
  Simply: int callback_func(struct ap_net_connection_t *conn, int signal_type). Signal_type is of AP_NET_SIGNAL_*
  The return value of this function should be true/false for user acknowledge to accept new connection and ignored in most other cases.
Then creating listener:
if ( ! ap_net_conn_pool_set_str_addr(pool, (char *)BIND_ADDRESS_STRING, LISTENER_PORT)
|| -1 == ap_net_conn_pool_listener_create(pool, MAX_TRIES, RETRY_SLEEP)
)
report_error();
- ap_net_conn_pool_set_str_addr() sets listener binding IP address from string form and integer port.
- ap_net_conn_pool_listener_create() binds and issues listen() call for TCP pool.
  MAX_TRIES parameter set count of retry attempts on bind() call. This is useful on system start-up when daemon can be loaded prior to networking interface initialization.
  The companion RETRY_SLEEP parameter sets sleep() seconds count between tries.
Now we have ready to process incoming connections pool.
And by running something like:
for(;;)
{
if ( ! ap_net_conn_pool_poll(pool) )
report_error();
}
That's nearly all what is needed.
Don't forget the callback:
int my_callback(struct ap_net_connection_t conn, int signal_type)
{
switch(signal_type)
case AP_NET_SIGNAL_CONN_CREATED:
/* connection structure is just got created.
This is not actual network connection event.
Time to attach your data to the connection's hook */
allocate_connection_user_data(conn);
break;
case AP_NET_SIGNAL_CONN_DESTROYING:
/* Connection structure is pending for removal.
Can be called on pool's array downsize.
Time to unhook your data binded with this connection */
free_connections_user_data(conn);
break;
case AP_NET_SIGNAL_CONN_CONNECTED:
/* Ah. This is out outgoing connection attempt made succesful */
send_first_packet_as_client(conn);
break;
case AP_NET_SIGNAL_CONN_ACCEPTED:
/* And this is new incoming connection established
and waiting our approval */
if ( ! check_if_we_want_this_client_at_all(conn) )
return 0;
initialize_connection_user_data(conn);
return 1;
case AP_NET_SIGNAL_CONN_CLOSING:
/* Closing by manual request, or peer graceful shutdown,
or any other event or fatal error
Maybe it's time to unhook your data too */
stop_data_processing_for_connection(conn);
break;
case AP_NET_SIGNAL_CONN_DATA_IN:
/* Some bytes arrived. You do something */
process_incoming_data(conn);
break;
case AP_NET_SIGNAL_CONN_TIMED_OUT:
/* if expiration is set to non-zero millisecs on pool creation
or manually corrected in the connection itself, then this signal
will arrive when it's less that current clock */
notify_of_slow_client(conn);
/* next and the last signal for this connection
will be AP_NET_SIGNAL_CONN_CLOSING */
break;
} /* end of switch */
} /* end of callback() */
The mentioned hook in connection's structure is void *user_data. On connection structure creation it initialized to NULL, so you can easy distinguish between hooked and not hooked.
The accepting procedure closes connection immediately after emitting AP_NET_SIGNAL_CONN_ACCEPTED signal if callback returned false.
Default expiration for incoming connections is set in ap_net_conn_pool_create() call. The actual expiration time is corrected on accept and connect events to be current time + pool default. If default is set to 0, no expiration is performed automatically. Beware of stalled connections! You can use ap_utils_timespec_* function set to manipulate conn->expire value.
Check for error and other states in bit-field conn->state. See AP_NET_ST_* in ap_net.h for description.
Upon receiving event for incoming data, ap_net_conn_pool_poll() automatically calls ap_net_conn_pool_recv() function that tries to receive data into connection's buffer. Upon arrival of some bytes, they are placed starting from conn->buf + conn->buffill position if there is some space left.
After that conn->buffill is added with count of bytes placed. That is your high watermark. The low watermark is conn->bufpos.
It is mandatory that you update this marker upon processing of some data. It's state is monitored and if it is past conn->buffill,
then buffer is considered "empty" and new data will arrive from the start of it. The bufpos value is set to zero then.
So the main rule is not to use some direct-to-buffer char* pointers as the data can be moved or replaced within poll() calls.
Always check bufpos and buffill variables. Also you can force leftovers of data cleaning by setting buffill to zero.
And that's basically the core of process, that will allow you to start.
For the bulk and details also check ap_net/ap_net.tests.c
# Section 2. ap_log - logging and debugging
This facility is light and clean. There is two nice global variables:
1. int ap_log_debug_to_tty - Boolean flag telling whether to output debug messages to stderr along with other registered debug channel(s)
2. int ap_log_debug_level - Verboseness of debug messages. This is used inside the guts of toolkit to show something from time to time, so be prepared that this will be not only your messages.
   Use if ( ap_log_debug_level >= MINLEVEL ) say_something; */
First you should register your opened file or socket descriptor as debug messages output target.
Multiple targets allowed at once. That way your messages can go to the console, log file and to the pair of remote stuff members that did telnet to your software's debugging port.
The debug_handle group is used to add or remove file or socket descriptors to the debug output list:
- int ap_log_add_debug_handle(int fd) - registers file/socket handle for debug output
- int ap_log_remove_debug_handle(int fd) - removes handle from debug output targets list
- int ap_log_is_debug_handle(int fd) - checks if handle is registered for debug output
Second, you can start writing your messages with:
- void ap_log_debug_log(char *fmt, ...) - printf() style logs something to the debug channel(s)
- void ap_log_debug_log_output(char *buf, int buflen) - writes pure buf content into debugging channel(s)
Additionally there is common syslog facility wrapper:
void ap_log_do_syslog(int priority, char *fmt, ...) that put your message to syslog also calls ap_log_debug_log() if ap_log_debug_level is > 0
In case of error occurred inside of toolkit function, you can get it's number by calling int ap_error_get(void), with code 0 means no error (see ap_error/*.h for list of AP_ERROR definitions.
Complement function is const char *ap_error_get_string(void) that returns string with info on last error occurred.
It return function name where error was caught, definition of error and system errno + strerror() call result if there was actually a problem with some system call.
The ap_log_h* set is designed to be much like fprintf/fputs/fputc standard calls, but instead of FILE* argument type it works with integer file or socket descriptor.
- int ap_log_hprintf(int fh, char *fmt, ...) - like fprintf()
- int ap_log_hputs(char *str, int fh) - like fputs()
- int ap_log_hputc(char c, int fh) - like fputc()
And ap_log_mem_* group is for raw memory area byte values display:
- void ap_log_mem_dump_to_fd(int fh, void *p, int len) - hexadecimal dump with printable chars into specified file handle
- void ap_log_mem_dump(void *p, int len) - hexadecimal dump with printable chars to debug channel(s)
- void ap_log_mem_dump_bits_to_fd(int fh, void *p, int len) - bits values dump into specified file handle
- void ap_log_mem_dump_bits(void *p, int len) - bits values dump into debug channel(s)
# Section 3. ap_str - strings manipulation. Parsing and tokens
The main functions set is ap_str_parse* which is wrapper around strtok(), plus some additional marvels:
- ap_str_parse_rec_t *ap_str_parse_init(char *in_str, char *user_separators) - creates new parsing record from in_str, using user_separators if not NULL or 'space' and 'tab' characters as default.
  The in_str is copied into parsing record, so you may re-use it after this call.
- void ap_str_parse_end(ap_str_parse_rec_t *r) - destroys parse record, freeing internal memory allocations
- char *ap_str_parse_next_arg(ap_str_parse_rec_t *r) - return next token or NULL if end of string
- char *ap_str_parse_get_remaining(ap_str_parse_rec_t *r) - get remnants of string without parsing it
- char *ap_str_parse_rollback(ap_str_parse_rec_t *r, int roll_count) - rolling n tokens back, restoring unparsed string. Reparses string at the requested point and returns token.
- char *ap_str_parse_skip(ap_str_parse_rec_t *r, int skip_count) - skip n tokens forward. Returns token.
- int ap_str_parse_get_bool(ap_str_parse_rec_t *r) - treats next token as textual Boolean value and returns Boolean value of it. -1 in case of error. Recognized words is on/off, 1/0, true/false, enable/disable
Other functions:
- void *ap_str_getmem(int size, char *errmsg) - A malloc with error checking. In case of error, if errmsg != NULL it is reported via ap_log_do_syslog() and exit(1) is called in the end
- int ap_str_makestr(char **destination, const char *source) - strdup()-like, but with auto free/malloc calls for destination. if it is NULL, then it's being allocated and strcat()-ted. If it is not NULL, then free() is called upon it, then malloc() and strcat(). Used for storing some default value first and replacing it with more actual data later.
- int ap_str_fix_buf_size(char **buf, int *bufsize, int *bufpos, int needbytes) - checks if designated buffer can hold additional data of specified size and if not the realloc() is called and bufsize is updated
- int ap_str_put_to_buf(char **buf, int *bufsize, int *bufpos, void *src, int srclen) - puts some data into buffer, calling ap_str_fix_buf_size() first, to check and fix, then srclen bytes is copied into buf, starting with bufpos offset
# Section 4. ap_utils - Miscellaneous utilities.
We have here one big set of time-related functions dealing with struct timeval and struct timespec
struct timeval ones:
- int ap_utils_timeval_cmp_to_now(struct timeval *tv) - performs *tv versus current clock comparison, returning -1 if *tv is less, 0 if == now and 1 if past current time
- int ap_utils_timeval_set(struct timeval *tv, int mode, int msec) - corrects or sets *tv value depending on mode, using msec as milliseconds count or offset. The modes are:
- AP_UTILS_TIME_ADD - adds msec amount to *tv current value
- AP_UTILS_TIME_SUB - subtracts msec amount from *tv current value
- AP_UTILS_TIME_SET_FROM_NOW - set *tv value to current time + msec
- AP_UTILS_TIME_SET_FROMZERO - set value to msec milliseconds
struct timespec ones. Used as time values holding structures inside the ap_net module
- int ap_utils_timespec_cmp_to_now(struct timespec *ts) - performs *ts versus current clock comparison, returning -1 if *tv is less, 0 if == now and 1 if past current time
- void ap_utils_timespec_clear(struct timespec *ts) - sets *ts value to zero
- int ap_utils_timespec_set(struct timespec *ts, int mode, int msec) - same as ap_utils_timeval_set()
- int ap_utils_timespec_is_set(struct timespec *ts) - returns true if *ts is not zero
- void ap_utils_timespec_add(struct timespec *a, struct timespec *b, struct timespec *destination) - Simply calculates *destination = *a + *b
- void ap_utils_timespec_sub(struct timespec *a, struct timespec *b, struct timespec *destination) - Simply calculates *destination = *a - *b
- long ap_utils_timespec_elapsed(struct timespec *begin, struct timespec *end, struct timespec *destination) - Counts elapsed time *destination = *end - *begin. begin or end can be NULL, in which case missing one is replaced in calculation by current clock value. For example if the end is NULL then we get *destination = now - *begin. destination can be NULL too if you only need returned milliseconds value.
- long ap_utils_timespec_to_milliseconds(struct timespec *ts) - Return *ts value as milliseconds
Other functions and features:
- uint16_t count_crc16(void *mem, int len) - do standard CRC16 calculation of memory area of length len
- bit_get(p,m), bit_is_set(p,m), bit_set(p,m), bit_clear(p,m), bit_flip(p,m), bit_write(c,p,m), BIT(x) (1 << (x))
  is macros for bit fields manupulation
End of document.
AP's Toolkit is Copyright 2013 by Andrej Pakhutin kadavris<at>gmail.com